## Slide 3
Service | PID | Description
01 | 00 | List of supported PIDs (01-20)
01 | 01 | Monitor status since DTCs cleared (includes MIL status and number of DTCs)
01 | 02 | Freeze DTC
01 | 03 | Fuel system status
01 | 04 | Calculated engine load
01 | 05 | Engine coolant temperature
01 | 0C | Engine RPM
01 | 0D | Vehicle speed
01 | 0F | Intake air temperature
01 | 11 | Throttle position
01 | (Same as Service 01 PIDs) | Show freeze frame data (data captured when a fault is detected)
01 | N/A | Show stored Diagnostic Trouble Codes (DTCs) (No PIDs, just request the service)
01 | N/A | Clear/reset stored emissions-related diagnostic information (No PIDs, just request the service)
01 | 00 | List of supported PIDs for Service 09
01 | 01 | VIN (Vehicle Identification Number) Message Count
01 | 02 | VIN (Vehicle Identification Number)

## Slide 5
DTC Code | Description | Troubleshooting Guide
P0001 | Fuel Volume Regulator Control Circuit/Open | - Check the fuel volume regulator wiring and connectors.<br>- Inspect the fuel pressure regulator.
P0100 | Mass or Volume Air Flow Circuit | - Check the MAF sensor's wiring and connectors.<br>- Clean or replace the MAF sensor if it's dirty or faulty.
P0171 | System Too Lean (Bank 1) | - Inspect for vacuum leaks.<br>- Check the fuel injector operation.<br>- Examine the oxygen sensors.
P0300 | Random/Multiple Cylinder Misfire Detected | - Check spark plugs and spark plug wires.<br>- Inspect the ignition coils.<br>- Look for any vacuum leaks.
P0420 | Catalyst System Efficiency Below Threshold (Bank 1) | - Inspect the catalytic converter.<br>- Check the rear and front O2 sensors.<br>- Look for exhaust leaks.
P0455 | Evaporative Emission System Leak Detected (large leak) | - Check the fuel cap (often a loose cap is the culprit).<br>- Inspect the EVAP system for leaks.
P0456 | Evaporative Emission System Leak Detected (small leak) | - As with P0455, check the fuel cap.<br>- Use a smoke machine to find tiny leaks in the EVAP system.
P0500 | Vehicle Speed Sensor A | - Check the speed sensor's wiring and connectors.<br>- Inspect the speedometer and instrument cluster.
P0700 | Transmission Control System Malfunction | - Inspect the transmission control module.<br>- Check for other transmission-related DTCs that might provide more specifics.
C0035 | Left Front Wheel Speed Circuit Malfunction | - Inspect the ABS sensor on the left front wheel.<br>- Check the sensor's wiring and connectors.
B0100 | Electronic Front End Sensor Fault | - Inspect the front end sensors and their wiring.<br>- Check for damage to the front bumper or collision-related issues.
U0001 | High-Speed CAN Communication Bus | - Check the CAN bus wiring for shorts or opens.<br>- Inspect the CAN bus terminators at both ends of the bus.